## Slide 1: GAMES103: Intro to Physics-Based Animation
Linear Finite Element Method
Huamin Wang
Dec 2021

## Slide 2: Topics for the Day
The linear finite element method (FEM)
The finite volume method (FVM)
Hyperelastic models

## Slide 3: Linear Finite Element Method

## Slide 4: The Linear FEM Assumption
In a nutshell, linear FEM assumes that for any point in the reference triangle, its deformed correspondence is: .
Reference (undeformed)
Current (deformed)
constant matrix
constant translational vector
, known as deformation gradient
For any vector between two points, we can use to convert it from reference to deformed:
.

## Slide 5: Deformation Gradient
Therefore, we can calculate the deformation gradient by edge vectors.
Problem: is related to deformation, but it contains rotation.
Reference (undeformed)
Current (deformed)

## Slide 6: Green Strain
Ideally, we need a tensor to describe shape deformation only. Recall that SVD gives , where only and are relevant to deformation.
Rotation
Rotation
Scaling
So we get rid of as: , Green strain.
If no deformation, ; if deformation increases, increases.
Three deformation modes: , and .
is rotation invariant: if additional rotation , then deformation gradient is but green strain is the same: .

## Slide 7: Strain Energy Density Function
Let be the the green strain describing deformation. We consider the energy density per reference area as: .
Total energy:
Constant within the triangle
The Saint Venant-Kirchhoff Model (StVK)
and are Lamé parameters.
Second Piola-Kirchhoff tress tensor,
something about force

## Slide 8: Forces
Given everything we have, we can now calculate the forces.
As in stress

## Slide 9
Recall that,
By definition,
So:
Forces

## Slide 10
Together, we get:
Forces
deformation gradient
Second Piola-Kirchhoff Stress

## Slide 11: Implementations
More details?
  Volino et al. 2009. A simple approach to nonlinear tensile stiffness for accurate cloth simulation. TOG
  Only talks about cloth (2D reference -> 3D deformation)
What about tetrahedron (3D reference -> 3D deformation)?
  Same idea, but everything is now in 3D.
  Deformation gradient
  Green strain
  Stress tensor
  Forces
  Messy code…

## Slide 12: Finite Volume Method

## Slide 13: Traction and Stress
First, let’s consider traction t: the internal force per unit length (area).
Interface L
Total interface force:
Stress tensor (interface normal -> traction):
So,

## Slide 14: The Finite Volume Method
FVM considers force calculation in an integration perspective, not a differentiation perspective.
midpoint
Interface L
Interface L20
Interface L10
Force contributed by an element:
Since is constant within the element,
(Divergence Theorem)
We know the force is:

## Slide 15: The Finite Volume Method
In 3D, FVM works in the same way.
Force:

## Slide 16: This stress is not that stress
Although the use of stress tensor is the same: mapping from the interface normal to the traction, it can be defined by different configurations.
In FEM, we define the energy density in the reference state. Therefore, this stress is a mapping from the normal to the traction , both in the reference state.
In FVM, we need to convert the normal into for force calculation. Therefore, this stress assumes the normal and the traction are in the deformed state.
Reference (undeformed)
Current (deformed)

## Slide 17: Different Stresses
We can now have different stresses, serving the same purpose but in different forms.
Traction in the reference state (unformed) |  | 
Traction in the current state (formed) |  | 
Input
Output

## Slide 18: Area Weighted Normals
Now let’s figure out the relationship between and , the two area weighted normals.
Reference
Current

## Slide 19: Different Stresses
We can now have different stresses, serving the same purpose but in different forms.
Traction in the reference state (unformed) |  | 
Traction in the current state (formed) |  | 
Input
Output
Force in the current state

## Slide 20: The Finite Volume Method
Anyway, now we have the following formula for force calculation.
Force:
Constant, can be precomputed
, as in previous FEM formulation
Second Piola–Kirchhoff stress:

## Slide 21: The Finite Volume Method
Think about more…
Meanwhile,

## Slide 22: Therefore,
We get:

## Slide 23: A Quick Summary (cont.)
A FEM/FVM Framework
Deformation gradient
Green strain
Second PK Stress
Forces

## Slide 24: After-Class Reading
Teran et al. 2003. Finite Volume Methods for the Simulation of Skeleton Muscles. SCA.

## Slide 25: After-Class Reading (Optional)
Volino et al. 2009. A Simple Approach to Nonlinear Tensile Stiffness for Accurate Cloth Simulation. TOG.

## Slide 26: Hyperelastic Models

## Slide 27: First Piola–Kirchhoff stress
We treat the first Piola–Kirchhoff stress tensor as a function of deformation gradient :
It converts an interface normal in the reference state to a traction in the deformed state.
Rotation
Rotation
Scaling

## Slide 28: Rotation-Invariance
The stress tensor is rotation-invariant to :
Rotation

## Slide 29: Isotropic Materials
The stress tensor is rotation-invariant to :
Rotation
Scaling
Scaling

## Slide 30: Isotropic Materials
Together, we claim:
Principal stretches: the singular values of
In many literatures, people parameterize by principal invariants, for:
is the right Cauchy-Green deformation tensor.

## Slide 31: Isotropic Models
The Saint Venant-Kirchhoff model (StVK):
The neo-Hookean model:
The Mooney-Rivlin model:
The Fung model:
Against shearing
Against bulky change (volume change)

## Slide 32: The Limitation of StVK
Irving et al. 2004. Invertible Finite Elements For Robust Simulation of Large Deformation. SCA

## Slide 33
Descent Methods for Elastic Body Simulation on the GPU (SIGGRAPH Asia 2016)

## Slide 34: Poisson Effects

## Slide 35: Model Behaviors

## Slide 36: Isotropic Materials
It can then be shown [Irving et al. 2004] that:
And we compute the first Piola-Kirchhoff stress as:

## Slide 37: A Quick Summary (cont.)
A FEM/FVM Framework
Deformation gradient
Principal stretches
Second PK Stress
Forces

## Slide 38: A Summary For the Day
FEM uses the derivates of the strain energy function to obtain the force.
FVM uses the integral of the interface traction to obtain the force.
The two approaches lead to the identical outcome, in two different formulations. FVM is more implementation friendly.
Hyperelastic models define the strain energy function by principal stretches, i.e., the singular values of the deformation gradient.
For isotropic materials, we can simply the stress through diagonalization.